Capillary Fan Controller Instructions

A) Assemble the supplied dial and dial spacer onto the controller unit using the 2 machine screws provided.

The probe can be installed either into the top hose or into a suitable threaded female housing in the engine or thermostat block.

A1) Probe installation in top hose:

- With the motor cold drain enough coolant out of the radiator so as the top hose can be removed (NB Coolant is a potentially hazardous fluid, drain into container & dispose of responsibility. Never attempt to open radiator cap or remove hose while motor is hot.)

- Remove radiator clamp & hose

- Insert probe into radiator hose

- If radiator hose is hardened or cracked due to ageing it may not seal around the probe - replace with new hose

- Retorque hose clamp & check coolant level, refill as required.

A2) Probe installation in suitable threaded housing:

  - With the motor cold drain coolant out.  (NB Coolant is a potentially hazardous fluid, drain into container & dispose of responsibility)

  - Identify a suitable threaded female housing to take sender probe, if no suitable housing pre-exists then one may be drilled & tapped – a choice of male adapter threads is supplied for this purpose

  - Torque sender adapter with suitable spanner

B) Locate & fix suitable position for controller unit. Note capillary tube cannot be lengthened or shortened

C) Disconnect positive lead on vehicle battery

D) Assuming that an electric fan(s) has or will be fitted attach the fan negative lead to a suitable earth

E) The controller may be hard wired (to a permanent live) or ignition wired (power will be cut when the ignition is off). Find a suitable power source according to your vehicle wiring diagram.

F) Power source (live or ignition switched live) should be connected to the terminal marked “C”. Supply to the fan should be connected to terminal marked “2” . Should you require a dashboard mounted tell-tale light (not included in kit) this may be connected to terminal marked “1”

G) Reconnect the battery positive lead, start and run the engine to operating temperature

H) Adjust the temperature at which the fan is switched on by means of the dial. To increase the turn-on temperature turn the adjuster clockwise.

Please note:

- These instructions are generic – they are not designed to cater for every fitting eventually on every vehicle, Motorsport applications in particular may wish to disregard these fitting instructions

- Installation should only be performed by an autoelectrician or other competent person

- Always employ standard precautions when working on a vehicle such as the use of safety goggles or other suitable eye protection, do not undertake fitting except in a well-lit area on level ground with vehicle handbrake or chocs applied, after installation check all vehicle functions thoroughly, before starting motor ensure that no tools or other items are left under the bonnet which may interfere with or be drawn into motor moving parts